## Slide 1
Jan 23 Sprint
10

## Slide 2: Process Safety Dashbaord App
Add “DP Health” Barrier stream
2 dummy wells with the dynamic positioning system data - 1 for Proteus and 1 for Thalassa (see screenshots below). Let me know if you have any questions or issues accessing
Dynamic Positioning – If any yellow then yellow, if any red then red.
  Alerts - Green
  Excursion -green
  DP Power -Green
  DP Thrust - Green
Dynamic Position

## Slide 3: Dynamic Position
Data
3155 - Derived by Sniffer\ AKA Derived Value\ Vessel Operating in Fault Tolerant Configuration
3163 - Derived by Sniffer\AKA Derived Value\ Plant Overloaded Alarm
3157 - Derived by Sniffer\AKA Derived Value\ Low Confidence in Data Logging System
Excursion – TBD
DP Power – TBD
DP Thrust - TBD
Processing
If 3155 or 3163 > 0 then red, otherwise green
If 3157 > 0 then yellow, otherwise green
If both of above are >0 then red
See slide 5
See slide 6
See slide 7
Display
Fleet overview
Work Unit Process Safety Dashboard
Measures the health of the Vessels power, thrusters, and location system

## Slide 4: Dynamic Positioning
Measures the health of the Vessels power, engines, and location systems
To assess Dynamic position, need some details to be added into system
Vessel/ Work Unit are not well specific and can change
Well Specific details update every well
Dynamic Position Application |  | Background
Vessel |  | Vessel drop down, based on Corva workunit identification
Number of Generators | 6 | Drop down list - 4, 6, 8, or 10 as options
Number of Thrusters | 6 | Drop down list - 4, 6, 8, or 10 as options
Individual Generator Maximum Power (kW) |  | Numerical entry No decimal
Generator Degraded % | 45% | Numerical entry 0-100
Individual Thruster Power output (kW) | 200 | Numerical entry No decimal
Thruster Degraded % | 60 | Numerical entry 0-100
Thruster Emergency % |  | 
Well Set up |  | Background
Well |  | Well drop down based on Corva Set up
DP SetPoint Latitude Degrees (364000 feet) |  | Numerical entry
DP SetPoint Longitude Degrees (364000 feet) |  | Numerical entry
DP SetPoint Latitude Minutes (6068 ft) |  | Numerical entry
DP SetPoint Longitude Minutes (6068 ft) |  | Numerical entry
Excusion Degraded (length) | 3 | Numerical entry
Excursion Emergency (length) | 23.8 | Numerical entry
Propose Shell create in Dev Center
Propose Corva create as part of Well setup

## Slide 5: DP Excursion
Measures the health of the Vessels power, thrusters, and location systems
Category | Source | Wits-DATA TAG | Wits Address | Description | Processing
Excursion | WITS | WITS_DATA_31_27 | 3127 | Latitude Degrees (364000 feet) | "X" = 364000*absolute value of (3127-"DP setpoint Latitude degrees") + 6068*absolute value of (3129 - "DP setpoint latitude Minutes")
Excursion | WITS | WITS_DATA_31_28 | 3128 | Longitude Degrees (364000 feet) | "Y"= 364000*absolute value of (3128-"DP setpoint Longitude degrees") + 6068*absolute value of (3130 - "DP setpoint longitude Minutes")
Excursion | WITS | WITS_DATA_31_29 | 3129 | Latitude Minutes (6068 ft) | "Excursion" = square root (X^2 +Y^2)
Excursion | WITS | WITS_DATA_31_30 | 3130 | Longitude Minutes (6068 ft) | If "Excursion" is > "Excursion Degraded" then Yellow
Excursion | Well Setup |  |  | DP SetPoint Latitude Degrees (364000 feet) | If "Excursion" is >or = "Excursion Emergency" then Red
Excursion | Well Setup |  |  | DP SetPoint Longitude Degrees (364000 feet) | 
Excursion | Well Setup |  |  | DP SetPoint Latitude Minutes (6068 ft) | 
Excursion | Well Setup |  |  | DP SetPoint Longitude Minutes (6068 ft) | 
Excursion | Well Setup |  |  | Excusion Degraded (length) | 
Excursion | Well Setup |  |  | Excursion Emergency (length) | 

## Slide 6: DP Power
Measures the health of the Vessels power, thrusters, and location systems
Category | Source | Wits-DATA TAG | Wits Address | Description | Processing
Power | WITS | WITS_DATA_30_13 | 3013 | Port Switchboard (FS37)\Generator 1 (A06)\ Generator Active Power | if any are < 1 then Yellow
Power | WITS | WITS_DATA_30_19 | 3019 | Port Switchboard (FS37)\Generator 2 (A07)\ Generator Active Power | "Max Power" = "Number of generators" * "Individual Generator Maximum Power"
Power | WITS | WITS_DATA_30_35 | 3035 | Centre Switchboard (FS39)\Generator 1 (A02)\ Generator Active Power | "Degraded Power" = "Max Power" * "Generator Degraded %"
Power | WITS | WITS_DATA_30_41 | 3041 | Centre Switchboard (FS39)\Generator 2 (A03)\ Generator Active Power | If 3013+3019+3035+3041+3069+3075 are >= "Degraded Power", then Yellow
Power | WITS | WITS_DATA_30_69 | 3069 | Starboard Switchboard (FS41)\Generator 1 (A06)\ Generator Active Power | 
Power | WITS | WITS_DATA_30_75 | 3075 | Starboard Switchboard (FS41)\Generator 2 (A07)\ Generator Active Power | 
Power | DP App |  |  | Number of Generators | 
Power | DP App |  |  | Individual Generator Maximum Power (kW) | 
Power | DP App |  |  | Generator Degraded % | 

## Slide 7: DP Thrust
Measures the health of the Vessels power, thrusters, and location systems
Category | Source | Wits-DATA TAG | Wits Address | Description | Processing
Thruster | WITS | WITS_DATA_30_02 | 3002 | Port Switchboard (FS37)\Thruster 4 (Port Stern Thruster) Feeder (A02)\ Thruster 4 Active Power | if any are < 1 then Yellow
Thruster | WITS | WITS_DATA_30_26 | 3026 | Port Switchboard (FS37)\Thruster 1 (Centre Bow Thruster) Feeder (A10)\ Thruster 1 Active Power | "Max Thrust" = "Number of thrusters" * "Individual Thruster Power Output"
Thruster | WITS | WITS_DATA_30_45 | 3045 | Centre Switchboard (FS39)\Thruster 3 (Starboard Bow Thruster) Feeder (A04)\ Thruster 3 Active Power | "Degraded Thrust" = "Max Thrust" * "Thruster Degraded %"
Thruster | WITS | WITS_DATA_30_50 | 3050 | Centre Switchboard (FS39)\Thruster 6 (Centre Stern Thruster) Feeder (A07)\ Thruster 6 Active Power | If 3002+3026+3045+3050+3058+3085 are >= "Degraded Thrust", then Yellow
Thruster | WITS | WITS_DATA_30_58 | 3058 | Starboard Switchboard (FS41)\Thruster 2 (Port Bow Thruster) Feeder (A02)\ Thruster 2 Active Power | 
Thruster | WITS | WITS_DATA_30_84 | 3084 | Starboard Switchboard (FS41)\Thruster 5 (Starboard Stern Thruster) Feeder (A11)\ Thruster 5 Active Power | 
Thruster | DP App |  |  | Number of Thrusters | 
Thruster | DP App |  |  | Individual Thruster Power output (kW) | 
Thruster | DP App |  |  | Thruster Degraded % | 

## Slide 8: Actions
Create the Dynamic position barrier stream – Nitish/Mohd
Code the “DP alerts” portion - Nitish/Mohd
Replicate “null” = grey for all barrier streams - Mohd
Set up DP static data with CSV – Tyler
Understand flowback application for alerts - Tyler